## Slide 1
Side-Channel-Secure
ARM32 Instruction Scheduling
A comparative study of Bayesian inference, CSP, and Reinforcement Learning
Mohamed Tajani
INFO-H410 — Artificial Intelligence
Université Libre de Bruxelles · 2025-2026

## Slide 2
The problem
Why naïve scheduling leaks your secret
Boolean masking splits a secret:
s = A ⊕ B
On an in-order pipeline (Cortex-M3/M4), if instructions on share A and share B are issued within k cycles, the register file holds both intermediates simultaneously.
→ Hamming-distance leakage in the power trace. First-order resistance broken.
Pipeline (k = 3)
A
B
·
·
A
B
⚡ leakage
safe (Δt ≥ k)
Real-world impact
Power-analysis attacks on naïvely-compiled masked AES recover full keys in minutes (Kocher 1999, and 25 years of follow-up).
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
2 / 12

## Slide 3
Formal problem
Scheduling as constrained optimisation
Given a basic block I = {I₀, …, I_{n-1}}, assign a start cycle tᵢ to every instruction.
RAW
Read-After-Write
t_j ≥ tᵢ + ℓᵢ
If j depends on i, j cannot start before i finishes (ℓ = latency).
SEC
Security distance
|tᵢ − t_j| ≥ k
Different shares (A vs B) must be separated by at least k cycles.
SLOT
One per cycle
tᵢ ≠ t_j
In-order, single-issue pipeline: one instruction per cycle.
Objective: minimise the makespan max(tᵢ + ℓᵢ) — equivalently, minimise the number of inserted NOPs.
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
3 / 12

## Slide 4
Why three AI techniques?
Three paradigms, one problem
The problem is NP-hard but its structure maps naturally to three different paradigms covered in INFO-H410:
A
Bayesian network
Probabilistic inference
soft, continuous risk
B
CSP / CP-SAT
Combinatorial optimisation
hard, optimal
C
MDP / DQN
Reinforcement learning
fast inference, learnt policy
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
4 / 12

## Slide 5
Approach A — Bayesian network inference
Soft probabilistic risk model
Idea
Side-channel leakage is not binary — it decays continuously with Δt.
Conditional Probability Table
Models the pipeline capacitor discharge:
Δt (cycles) | P(L = 1)
1 | ≈ 0.95
2 | ≈ 0.50
3 | ≈ 0.10
≥ 4 | ≈ 0.00
Greedy scheduling with risk threshold τ
1. Compute the marginal expected leakage E[L] for every data-ready candidate.
2. Pick the candidate that minimises E[L].
3. If even the best E[L] > τ (e.g. 0.15), inject a NOP. Δt grows, risk decays under τ.
Cost: O(n²) inference, no training.
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
5 / 12

## Slide 6
Approach B — Constraint Satisfaction (CP-SAT)
Declarative, optimal
Encoding
• Integer variables tᵢ ∈ [0, T_max]
• T_max from a greedy warm-start (tight upper bound).
• SEC encoded as reified disjunction:
(t_A − t_B ≥ k) ∨ (t_B − t_A ≥ k)
• Objective: minimise max(tᵢ + ℓᵢ).
Solver: Google OR-Tools CP-SAT
• SAT-based propagation + clause learning (CDCL).
• 4 parallel workers, free multi-core speed-up.
• Proven optimal for n = 10 in tens of ms.
• Best-effort under timeout (15 s) for n ≥ 30.
Fallback: python-constraint backtracking when OR-Tools is missing (limited to n ≤ 15).
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
6 / 12

## Slide 7
Approach C — MDP / Deep Q-Network
Learning a scheduling policy via reward shaping
Markov Decision Process formulation
State 6-D feature vector (block-size invariant): ratios of remaining work, distance to last A/B, ready-queue size, critical path.
Action Pick a ready instruction or insert NOP.
Reward −1 / cycle, −100 / violation (rescaled), +50 on completion.
Training stack
• MLP Q(s, a) on PyTorch (GPU when available).
• Experience replay (10 000), target net every 200 steps.
• ε-greedy: 1.0 → 0.05, decay 0.997.
• Huber loss, gradient clipping.
✓ Reward-shaping ablation (n = 10): rescaling −10 → −100 restores 100 % valid schedules within 6 % of the CSP optimum.
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
7 / 12

## Slide 8
Experimental setup
Same blocks, fair comparison
n ∈ {10, 30, 50}
Block sizes
k = 3
Security distance
3 seeds
42 / 43 / 44
1 toolchain
Identical block per (n, seed)
Metrics reported
• Makespan (total cycles)
• Number of inserted NOPs
• Expected leakage E[L] = Σ P(L=1) over all share-AB pairs
• Wall-clock solver time (training time reported separately for the MDP)
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
8 / 12

## Slide 9
Results at k = 3
Mean over 3 seeds — MDP † default reward, MDP ★ tuned reward (−100)
n | Method | Cycles | NOPs | E[L] | Valid
10 | Bayesian | 11.0 | 1.0 | 0.05 | 100 %
 | CSP | 11.0 | 1.0 | 0.03 | 100 %
 | MDP † | 10.3 | 0.3 | 1.40 | 0 %
 | MDP ★ | 11.7 | 1.7 | 0.13 | 100 %
30 | Bayesian | 31.7 | 1.7 | 0.12 | 100 %
 | CSP | 30.0 | 0.0 | 0.09 | 100 %
 | MDP † | 30.7 | 0.7 | 4.10 | 0 %
50 | Bayesian | 53.0 | 3.0 | 0.20 | 100 %
 | CSP | 50.0 | 0.0 | 0.15 | 100 %
 | MDP † | 50.7 | 0.7 | 8.50 | 0 %
Bayesian — low E[L] via τ; sub-ms inference; 5–10 % cycle overhead.
CSP — tightest makespan, zero NOPs at n = 30/50; timeout (15 s) for large blocks.
MDP ★ — rescaling penalty −10 → −100 restores 100 % valid at n = 10 (within 6 % of CSP).
* CP-SAT timeout reached — solution feasible but optimality not proven. † default reward (−10 / violation). ★ tuned reward (−100 / violation).
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
9 / 12

## Slide 10
Trade-offs
When to prefer each approach
Scenario
Bayesian
CSP
Comment
Strict cycle distance k required
~
✓✓
CSP encodes hard constraints natively
Code-density (minimum NOPs)
✓
✓✓
CSP minimises makespan globally
Sub-millisecond compile-time budget
✓✓
✗
CP-SAT can hit timeout at n ≥ 30
Soft / probabilistic threat model
✓✓
~
Bayesian models continuous risk via τ
Adding business rules (e.g. resource)
~
✓✓
CSP: one-line model change
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
10 / 12

## Slide 11
Conclusion
■ Three approaches, three regimes: Bayesian inference for soft, probabilistic threat models with sub-millisecond inference; CSP / CP-SAT for strict guarantees and tight makespans; MDP/DQN as a learnable scheduler once the reward is correctly shaped.
■ Reward-shaping is the lesson. Default penalty (−10 / violation) made it rational for the agent to ignore security at large n. Rescaling to −100 restores 100 % valid schedules at n = 10, within 6 % of the CSP optimum — a clean negative-then-positive ablation result.
■ Future work: extend the tuned MDP rerun to n = 30 / 50; extract CPTs from real Cortex-M4 power traces; explore a hybrid CSP + RL architecture where CSP acts as a feasibility oracle for the agent.
INFO-H410 · Side-Channel-Secure ARM32 Scheduling · Mohamed Tajani
11 / 12

## Slide 12
Questions ?
Side-Channel-Secure ARM32 Instruction Scheduling — INFO-H410 — Mohamed Tajani
Code & data: github.com/<user>/ARM32-Instruction-Scheduling
INFO-H410 · Université Libre de Bruxelles · 2025–2026